## Slide 2: Course: HEI Module Agricultural sustainability, management of natural resources and climate action Learning Unit Agricultural reuse of organic residuals
Author: UNIFI

## Slide 3
Introduction
The agricultural reuse of organic residuals represents a pioneering frontier in sustainable farming and environmental stewardship. It refers to the practice of recycling organic waste materials back into the agricultural system to enhance soil fertility, improve soil structure, and promote sustainable agricultural practices.
PROMOTION OF SUSTAINABLE AGRICULTURE AND…
Soil health
and fertility
Waste reduction and recycling
Regulatory compliance
Resource
efficiency
Cost
savings

## Slide 4
1
Typologies and characterization of agricultural residues
Organic residues that can be used agriculture are categorized based on their origin and composition
Crop residues
Livestock waste
Agro-industrial waste
Acquaculture waste

## Slide 5
Module: A / Learning Unit: 4 / Sub Unit: 1
Crops residue: stems, leaves, and other plant parts left on the field after harvesting. Variable composition
Silage Residues: residues from the ensiling process used to preserve forage crops.
Poultry Litter: Mixture of chicken droppings and bedding material.
Manure: animal waste, often mixed with bedding material, generated on farms
Wastewater Sludge: from treatment of agricultural or food processing wastewater. Careful handling due to potential contaminants
Food Processing Residues: byproducts generated during food processing
Aquaculture Residues: Waste generated from aquaculture activities.
Wood Residues: residues from wood processing industries or tree pruning
N/P
C/N/P/K
C/N/P
N/C
1
2
3
4
5
6
7
8

## Slide 6
At present, there are many ongoing research and EU-funded projects investigating solutions and technologies aimed at recovering not only useful nutrients in agriculture, but also elements and molecules for use in other sectors.
European NOMAD project
projectnomad.eu
There are experience and ongoing research on the use as a fertiliser of organic residues from bioenergy production processes.
Einterreg North-West Europe AgriWasteValue
To transform agricultural residues into bioactive compounds for industrial sectors as cosmetic and nutraceutical. Secondly into energy, chemical and agricultural fields
EU Horizon 2020
Rustica project
Technical solution to convert organic residues from fruit and vegetable into novel bio-based HQ fertiliser products that address the needs of modern agriculture
research and innovation

## Slide 7
Module: A / Learning Unit: 4 / Sub Unit: 1
Interesting tool that can be helpful in learning about the types of biomass and algorithms for calculating their potentials
© Institute of Soil Science and Plant Cultivation – State Research Institute in Pulawy, Poland.
This project has received funding from the European Union's Seventh Framework Programme for research, technological development and demonstration under the Grant number 282873.
BioBoost Geoportal
https://bioboost.eu/media/the-bioboost-project.html

## Slide 8
Biochar as a solution for sustainable agriculture
Biochar is a type of charcoal produced through the pyrolysis process (organic materials are heated in a low-oxygen environment). The result is the degradation of the materials into a carbon-rich substance. Biochar production is often carried out using various biomass sources, including wood chips, crop residues and other waste organic materials.
Trasportation & distribuition
Feedstock selection
Lack of standardization
Energy
consumption
Social/Ethical Concerns
KEY CHALLENGES
2

## Slide 9
Biochar can be produced from various organic waste materials, providing a way to recycle and repurpose agricultural residues, forestry waste, and other biomass
Benefits of biochar application in agriculture
(Source: European Biochar Industry Consortium)
what is biochar?
the biomass pyrolysis process

## Slide 10
safe handling and storage of biochar is essential to minimize potential risks and maximize its benefits
management practices
Biochar can generate dust, which may be harmful when inhaled. To minimize dust, moisten the biochar before handling or use wetting agens. This is also the best way to prevent your biochar from being lost to wind
Biochar is highly flammable, especially in fine particulate form. Keep fire extinguishers readily available and ensure that your storage area complies with fire safety regulations
Store biochar in a dry and well-ventilated area to prevent moisture absorption and the growth of moth or bacteria. Use sealed containers or bags to protect it from environmental contaminants.

## Slide 11
biochar works synergistically with organic matter. Incorporating biochar alongside compost or other organic materials enhances nutrient retention and improves soil microbial activity. Biochar can be used not only as soil amendment but also for contaminants filtration and erosion reduction.
where and how to put biochar
As soil amendment put biochar into the plant’s root zone incorporating the biochar into 4 to 6 inches of soil depth
With erosion reduction or contaminants filtration action place biochar where necessary (landscapes socks and filtration systems) e.g. where water is running off land, roots, roads or contaminated sites

## Slide 12
Organic residues management and logistic considerations
Effective residues management and logistics are essential components of modern agriculture and environmental stewardship. Planning, collection, and disposal are critical for both environmental sustainability and resource efficiency.
waste management hierarchy
First step towards a more sustainable resolution of the waste is to adopt a sustainable production and consumption approach along the global food supply chain.
Incineration of waste, even if with energy recover, should be considered as last option before the waste disposal.
We can do a lot to improve the way how we can reuse materials before they can be considered as waste.
3

## Slide 13
Waste incineration is often presented as a ‘quick-fix’ solution to reduce rapidly growing waste volumes while producing energy. However, incineration is among the worst approaches can taken to achieve both waste reduction and energy goals
the last option before the waste disposal…
1. Producing energy from solid waste (especially from organic waste) incineration is highly inefficient
waste is composed of about 70% water, and burning it requires considerable energy….
2. Incineration is the most expensive way to make energy
waste incineration is the costliest form of power generation, in terms of both the cost to build and to operate….
3. Waste incineration creates air pollution and requires strong environmental controls
when waste is burned it produces hazardous air pollutants including particulate matter, carbon monoxide, acid gases, nitrogen oxides….
energy produced from waste incineration is NOT clean or renewable

## Slide 14
how to manage food waste and organics on the path to zero waste
Focusing on cities and high populated areas, they are source of a big amount of organic waste, especially from food waste.
Set food and organic waste reduction goals: an absolute reduction, or a reduction in the total percentage of organics being sent to disposal
Include wider systemic benefits and revenue-generation potential: consider the revenue that can generated from the outputs of organic waste treatment systems, in particular by selling biogas, electricity, heat, digestate and compost
Develop and test a multi-approach strategy for organics collection with support of waste-management operators.
Incentives and nudges to encourage or require waste generators to separate organic waste: e.g. creating price differential, volume-based schemes (Pay-as-you-throw (PAYT)), providing more frequent organic collection
Investments in treatment technology that adequate for the specific situation and explore opportunities to leverage existing treatment infrastructure: locate a treatment facility close to the city and existing waste-management sites

## Slide 15
The EU Waste Framework Directive
The Waste Framework Directive sets the basic concepts and definitions related to waste management, including definitions of waste, recycling and recovery
by 2025, the preparing for re-use and the recycling of municipal waste shall be increased to a minimum of 55 %, 60% and 65% by weight by 2025, 2030 and 2035 respectively
by-products is a substance or object, resulting from a production process, the primary aim of which is not the production of that item. By-products can come from a wide range of sectors with different environmental impacts
the Waste Framework Directive provides additional labelling, record keeping, monitoring and control obligations from the "cradle to the grave"
End-of-waste criteria specify when certain waste ceases to be waste and becomes a product, or a secondary raw material
Directive 2008/98/EC

## Slide 16
The hidden cost of the food we throw out and that can be reused as organic matter

## Slide 17
Processes and treatments for successful reuse
The processes and treatments designed for the successful reuse of various materials in agriculture represent a dynamic and innovative realm at the intersection of environmental sustainability, resource efficiency, and agricultural productivity
NUTRIENT RECOVERY
From the main 3 losses streams
Livestock manure
Sewage sludge
Food chain waste
4

## Slide 18
Food chain waste
Food waste generation by sector, EU, 2012 (EEA Report n.04/2020)
In 2017, the EU-28 generated 249 million tonnes of municipal solid waste (Eurostat, 2019), of which about 34 % (86 Mt, around around 175 kg/capita/yr) was bio-waste.
Nutrients can be recovered from biodegradable waste through composting, anaerobic digestion and incineration. According to the European Commission, maximizing recovery and recycling could potentially substitute 10% of phosphate fertilisers with compost and reduce soil degradation by 3-7% due to the addition of organic matter.

## Slide 19
Livestock manure
Any excrement and/or urine of farmed animals other than farmed fish, with or without litter. The regulation establishes limitations on its handling, transport and traceability. Manure use on land is regulated by the Nitrates Directive (91/676/EEC), that establishes a threshold of 170 kg N/ha only in Nitrate Vulnerable Zones.
Direct manure application on agricultural fields is often driven by the motive to dispose conveniently of material considered a nuisance rather than valued as a nutrient. The dosage may not always be based on calculations of crop nutrient demand…
In general, nutrient recovery from manure implies dewatering, concentrating and converting manure into a stable product that can be easily stored, transported and applied.
Manure recovery processes use two types of substrates: raw manure or digested manure

## Slide 20
Sewage sludge
Sewage sludge is an organic substrate relatively rich in nutrients and trace elements. Sludge composition varies regionally and seasonally and there is little monitoring of the concentration and amounts of nutrients in sewage reaching Sewage Treatment Systems.
Anaerobic digestion is the most common treatment for sludge that is later applied to land. Anaerobic digestion stabilises the organic compounds in sludge and reduces the odour.
The biogas generated by the process can be used
internally in the plant or used to produce electricity.
Sludge is used in agriculture as a source of nutrients (N and P) for plants and also a way to replace organic matter back into the soil.
Sludge application to agricultural land is framed by the
directive on the use of sludge in agriculture (86/278/EEC).

## Slide 21
Composting
A natural biological process where microorganisms break down organic materials into a nutrient-rich soil conditioner. Organic waste, including kitchen scraps, yard waste, and crop residues, is mixed in proper proportions (carbon to nitrogen ratio), aerated, and regularly turned to promote decomposition.
The process can be enhanced introducing forced aeration (Aerated Static Pile (ASP) Composting) to increase oxygen supply and accelerate decomposition.
Organic waste is placed in a pile with aeration pipes, and a blower forces air through the pile. This method speeds up the composting process.

## Slide 22
Composting
Degraded land begins to bloom thanks to European composting projects
It is possible to recycle agricultural residues in organic farming by on-farm compost production
Correct starting mixture!
Chart: 
Vendite | 62 | 35 | 3
25% of all compost produced in the EU 27, CH, NO and UK is certified to the ECN’s quality insurance scheme. European Compost Network (ECN) is a European non-profit membership organisation promoting sustainable recycling practices in composting, anaerobic digestion, and other biological treatment processes of organic resources.
Temperature of the pile should be continuously controlled to evaluate the ending phase of the process (when the inside temperature approaches the external one).
The composting pile moisture should be checked weekly and kept between 40 and 70%.

## Slide 23
Anaerobic digestion
Process where microorganisms break down organic matter in the absence of oxygen, producing biogas (methane and carbon dioxide) and a nutrient-rich slurry. Manure, food waste, and wastewater solids are placed in a sealed, oxygen-free environment. The biogas generated can be used for energy, and the digested material (digestate) is a valuable fertilizer.
The four stages of the AD process
The biomass added to the digester is broken down into sugars, amino acids and fatty acids (hydrolysis), fermented to produce volatile fatty acids and alcohols (acidogenesis) followed by the conversion into hydrogen, carbon dioxide and ammonia and, finally methanogens produce biogas from acetic acid and hydrogen.
AD of food waste takes place at two optimum temperature ranges, 35-40°C (mesophilic) and 55-60°C (thermophilic

## Slide 24
Anaerobic digestion
Based on the constituents and consistency of the food waste treated, an anaerobic digester can be designed as
a ‘wet’, ‘dry’, ‘liquid’ or ‘co-digestion’ system
WET DIGESTION
Suitable for AD of most food wastes such as source segregated food waste collection from residents, commercial and industrial organic wastes from supermarkets, food processing plants and food services. The feedstock contains typically less than 15% dry solid matter.
DRY DIGESTION
Dry digestion is most suitable for organic waste with a higher component of solids such as food waste that is collected along with garden waste.
LIQUID DIGESTION
Liquid digestion is most suited for food and drink industries which generate large volumes of wastewater with low suspended solids such as effluent from breweries, sugar factories, drinks factories, starch factories, potato processing and confectionary.
CO-DIGESTION
Wastewater treatment plants
or recovery facilities which typically have high energy requirements benefit from the high energy value of food waste while food waste collectors benefit from any excess capacity of the wastewater treatment plants

## Slide 25
Anaerobic digestion
Digestate may be used whole or separated into solid and liquid parts. The solid fractions may be processed into compost and/or dried into dried solids for land application. The liquid fractions maybe concentrated into liquid fertiliser or partially treated and sent to a wastewater treatment facility or fully treated and discharged
Data source: 2018 World Biogas Association.

## Slide 26
The biowaste processing sector across EU
Data source: ECN rapport 2022.

## Slide 27
The biowaste processing sector across EU
Data source: ECN rapport 2022.
Projected value of compost sales by 2035 assuming doubling of imput feedstocks
Price per tonne of compost in millions euros

## Slide 28
The biowaste processing sector across EU
Anaerobic digestion plants are less labour intensive compared to composting, reflecting the differences in technologies and processing
Data source: ECN rapport 2022.

## Slide 29
Carbon recycling & soil improvement
All European soils suffer from erosion. 2% of arable land and 16% of modaretely eroded agricultural land could benefit from compost application at 10 ton/ha
Data source: ECN rapport 2022.
Most European countries don’t manufacture enough compost to apply to their eroded soils
Countreis that currently (2022) produce more than enough compost to apply to all of their eroded agri-cultural soils (10 ton/ha per annum)
The fraction of arable land could benefit from compost produced at currently estimated amount is very low

## Slide 30
Cost/benefit - from waste to opportunity
The cost and benefits associated with the reuse of organic waste can vary depending on factors such as the type of waste, the chosen reuse method, local regulations, and the specific goals of the reuse program
5
COSTS
Infrastructure Investment
establishing facilities initial investment in infrastructure, equipment, and technology
Transportation Costs
costs associated with vehicles, fuel, and labour
Operational Costs
labour, energy, maintenance, and monitoring
Regulatory Compliance
Meeting environmental regulations and standards may require additional investments in monitoring
Market Challenges
BENEFITS
Reduced Waste Disposal Costs
reduction of landfill disposal fees
Soil Improvement and Fertility
costs associated with vehicles, fuel, and labour
Energy Generation
Biogas for energy generation is an example
Economic Opportunities
Such as job creation in recycling facilities, the production of compost or bioenergy
Greenhouse Gas Reduction

## Slide 31
Advantage & disadvantages
overview on advantages and disadvantages related to the different management strategies of organic waste
Animal feed
Residues| Maize, sugarcane, grain, sorghum,soybean, wheat, and vegetables
PROS |Nutrient source for animals, Waste reduction
CONS |Toxicity in feeds due to the toxins produced by the crop itself or applied to the crop (e.g., insecticides or herbicides) and produced by molds and fungi
Composting
Residues| Leaves, grass clippings, plant debris, food scraps
PROS |Organic fertilizer, solves environ-mental problems, kills pathogens, reduce germination of weeds and odour, reduces landfill waste
CONS |Cost for site preparation and equipment can be high, lengthy treatment period, issues such as odours and dust

## Slide 32
Advantage & disadvantages
overview on advantages and disadvantages related to the main management strategies of organic waste
Mushroom
cultivation
Residues| Wheat straw, paddy straw, rice straw, rice bran, molasses, coffee straw, tea leaves, cotton straw, saw dust
PROS |Cost effective farming, practices to fight the malnutrition and environ-mental pollution caused by these wastes
CONS |Lack of available market and promotion in local level
Surface mulching
Residues| Bark chips, grass clippings, wheat or paddy straw, plant leaves, compost, rice hulls and sawdust
PROS |Prevents erosion, moderate soil temp. provide nutrients, kills pathogen and pests, increase water retention, ….
CONS | Keep the soil too moist on poorly drained soils (low oxygen), breeding spots for some pests, mulches (hay and straw) contain seeds which may become weeds

## Slide 33
Advantage & disadvantages
overview on advantages and disadvantages related to the main management strategies of organic waste
Biofuel
Residues| Rice (bioethanol), wheat (bioethanol) and corn straw (bioethanol) as well as sugarcane bagasse (biofuel)
PROS | Renewable, reduced dependence on fossil fuels, waste reduction
CONS | Cost for setting up biomass energy plant is expensive
Paper & pulp industry
Residues| Wheat straw, cotton rags, cotton linters, softwood
PROS | Less environmental impact than raw material processing, prevention of deforestation, constant waste residue availability
CONS | Lack of available market and proper promotion in local level

## Slide 34
European legislation on organic residuals reuse in agriculture
6
The European legislation on organic residuals reuse in agriculture is aimed at promoting sustainable agricultural practices and environmental protection. EU has a framework for waste management and recycling that includes organic residuals
Waste Framework Directive | (Directive 2008/98/EC) establishes principles and definitions related to waste, recycling, and recovery. It encourages the reuse of organic residuals where feasible
Circular Economy Action Plan | the European Green Deal and the Circular Economy Action Plan emphasize the importance of sustainable use and management of organic residuals in agriculture to reduce waste and promote resource efficiency
Specific regulations and guidelines may vary from one country to another within the EU. Local regulations can provide more detailed and region-specific guidance on the use of organic residuals in agriculture

## Slide 35
EU regulation on fertilising products (Reg. UE 2019/1009)
Applied since 16 July 2022, the new rules are boosting the role of the Single Market, help reduce the environmental impact of fertilisers, limit their risk on human health as well as reduce Europe’s dependency on imported fertilisers

## Slide 36
Some relevant points
EU regulation on fertilising products (Reg. UE 2019/1009)
Easier for producers of organic fertilisers and from recovery chains to sell products with harmonised quality standards for all types of materials that can be marketed throughout the European Union
More choice for farmers, reduced risks for the environment and consumer health.
The case of organo-mineral fertilisers with 'low cadmium content' <20 mg/kg allows for improved soil protection and reduced health and environmental risks compared to mineral fertilisers with high cadmium content.
Promotion of the use of organic and biological fertilisers derived from the recovery of waste materials.
Establishment of EU-wide quality, safety and environmental criteria for 'EU' fertilisers
Full harmonisation of the internal market will eliminate all costs related to mutual recognition and/or divergence of national standards, as well as ensuring a uniform level of protection of human health and the environment

## Slide 37
EU’s science-policymaking interactions
The European Commission’s Science Advice Mechanism (SAM) was created in 2016 to replace the Chief Scientiﬁc Advisor who was until then the sole scientiﬁc advisor, reporting directly to the President of the European Commission.
SAM is based on an expert Group of Chief Scientiﬁc Advisors nominated by the European Council